## Slide 1: Health Shops Training Zambia
Module 3: Session 9
The Use of RDT* for Malaria
*RDT = Rapid Diagnostic Tests

## Slide 2: NOTE
THIS SESSION IS A GENERIC FORMAT FOR TRAINING IN USE OF AN RDT. IT IS RECOMMENDED THAT THE PACKAGE LEAFLET OF THE ACTUAL RDT IN USE IN THE FACILITIES AT THE TIME OF CONDUCTING THIS TRAINING BE USED TO REFER DURING THIS SESSION

## Slide 3: Objectives
As a result of actively participating in this session, the individual will be able to:
  Demonstrate the RDT testing process.

## Slide 4: Rapid Diagnostic Tests
We must confirm all suspected cases of malaria by identifying the presence of parasites in the blood.
In a health shop setting, we can do this with the use of rapid diagnostic tests (RDT).
An RDT is accurate, simple to perform, and doesn’t require a microscope.

## Slide 5: How to Use an RDT: Step 1
Gather your materials
  Instruction sheet (package insert)
  Packaged cassettes
  Lancets
  Blood collection devices (dropper or micro-capillary tubes)
  Reagent buffer
  Swabs (70% alcohol, cotton wool, or gauze)
  Gloves
  Timer (watch or clock)

## Slide 6: How to Use an RDT: Step 2
Prepare for the test
  Read the instructions on how to use the malaria test kit carefully.
  Look for the expiry date at the back of the package. If the test kit has expired, use another cassette.
  Ensure the foil is not damaged by squeezing gently and feel/listen for air leakage. If the foil is damaged, use another cassette.
  Talk to the client and explain what you want to do.

## Slide 7: How to Use an RD: Step 3
Open the packaged cassette
  Open the package by tearing along the nick.
  Look for the following:
  c. Throw away the desiccant.
Desiccant
Cassette

## Slide 8: How to Use an RDT: Step 3 (cont.)
NOTE: the opened RDT looks like this:

## Slide 9: How to Use an RDT: Step 4
Draw the client’s blood.
  Ensure you are wearing gloves.
  Clean the client’s finger using alcohol swab.
  Allow the site to DRY.
  Prick the side of the client’s finger to get just a very small amount of blood.
Note: Dispose of the lancet in a sharps container.

## Slide 10: How to Use an RDT: Step 5
Transfer the blood to the cassette pad.
  Immediately touch the tip of the capillary tube with blood in the sample well of the cassette.
  Allow the blood to be drawn onto the cassette pad.
  Place dry cotton wool over the puncture site to stop the bleeding.
Note: Dispose of the capillary tube into a sharps container.

## Slide 11: How to Use an RDT: Step 6
Put five (5) drops of buffer into the buffer well.

## Slide 12: How to Use an RDT: Steps 7-8
7. Set the timer to 20 minutes.
8. Read the results exactly twenty (20) minutes after adding buffer.
Note: Do not read the results before or after 20 minutes.

## Slide 13: How to Use an RDT: Step 9
9. Interpret the results.
  Look in the window section of the cassette.
  If you see one red control line near mark “C”, the result is NEGATIVE – the person does not have malaria.
One control band near mark “C”

## Slide 14: How to Interpret the Results
9. Interpret the results (cont.)
  If you see two (2) red-coloured lines – one test line and one control line – near mark “C”, the result is POSITIVE – the person has malaria.
  d. If the control line fails to appear, the test is not valid and must be repeated. (The reagents may have expired or the procedure may have been done incorrectly.)

## Slide 15: Treat Appropriately

## Slide 16: Precautions
Ensure that RDTs are stored at room temperature (4 - 40º C).
Follow instructions given in the leaflet.
Use recommended sample and buffer volumes.
Do not open the foil until you are ready to do the test.

## Slide 17: Review of Objectives
Were we able to:
Demonstrate the RDT testing process.
Field practicum of RDT use to follow.